Directions for Types 24645, 24646,

24648, 24666

See that blades turn freely without touching

guard.

This fan is for alternating current only, of

voltage and cycles stamped on name-plate.

Screw   plug   into   socket;  start   by  moving

switch to point 1;  point 2  gives  slower speed;

point 3, slowest speed.

If fan does not start, turn off current at socket; see  that  connections  are  tight. Remove this

plate to examine connections inside.

Supply oil before starting, through oil cup at

back, raising cap of oil cup.  Oil fan monthly,

a little at a time, using oil furnished with fan;

never use lard, olive, cotton-seed or such oils.

Once a season put a few drops of oil on washer

above adjusting collar.

The gears at back of fan run in grease; no oil

is necessary. If they run dry or noisy, repack

gear case with good lubricating grease (not

vaseline).

To tilt fan loosen  wing  screw in ball of base.

Remove  wing  screw  and  readjust  base to angu-

lar position before fastening to wall. Do not run

fan blowing straight up or down.

See  that  wire  from  motor  to base is free to

bend in its entire length during oscillations, and

that ratchet handle does not strike cord while

rotating.

Noise  is  sometimes  due  to lack of oil or to

vibration of some object near by. Mention num-

bers on name-plate in referring to this fan.

Form 7115